## Slide 1: The Epoch FPGA Phone
Digilient North American Competition
David McGinnis & Kyle Green

## Slide 2: Background
No exposure to CSSE or ECE early in a child’s life
  This causes no motivation for entering the field later.
  We need something that teaches them, while tapping into a popular item.
  Also needs to grow with them, due to cost of technology.

## Slide 3: More Background
Smartphones are a hot commodity
Make a modifiable, open-source smartphone for grade school students
  Can be used originally for course work & organizational skills
  Later, kids can learn how to modify their phones
  Gives them feeling of accomplishment, while also encouraging them to enter CS and ECE fields.

## Slide 4: Overall Architecture
Assembler
The BitEpicness Processor
Phone Module
Resistive Touchscreen
VGA Adapter
SD Card Reader
Seven-Segment Display
Switch Inputs
Keyboard Input
MiniC Compiler
McOS Operating System

## Slide 5: Why FPGAs?
Software is easy to modify, but hardware is not.
FPGA gives ability to easily modify hardware
  Students can modify, and see what happens
  No worrying about electrical dangers such as blown capacitors or electrical shock.
Notes: Mention Picoblaze Processor

## Slide 6: Overall Features
32-bit MIPS-like Processor
16 MB of RAM
VGA Display Capabilities
Resistive Touchscreen Interface
Hardware Phone Interface
Keyboard Input
Switches and Displays for Debugging
C Compiler, Assembler and Custom OS

## Slide 7: The Epoch Processor
32-bit processor based on MIPS
16 bit instruction length
33 operations with 4 or 5 bit op codes
16 registers, 13 of which are general purpose registers
1KB Instruction ROM
Coprocessor with four registers
Operations chosen for flexibility
  All operations have register-based equivalents
  Allows 16-bit and 32-bit operation

## Slide 8: The BitEpicness Processor Architecture
Instruction Fetch/Decode
Register Fetch
Execute
Memory Fetch/Branch
Writeback

## Slide 9: Memory Management
CellularRAM used for instruction and data memories
For each CPU clock cycle, 3 values are read from memory

## Slide 10: I/O: The Port System
Simplistic, yet flexible
All operations are reduced to reading or writing to ports
Each I/O peripheral gets one port
  Software interrupts get any port larger than 32 representable by a 32-bit number
More complex operations use special structured commands

## Slide 11: VGA Module
320x256 resolution screen, with 3 bit color
GPU included for drawing
  Draws text, pixels, and colored boxes
  Adaptable to add more functionality

## Slide 12: Keyboard Module
Uses PS/2 port to receive input from keyboard
Scan codes from keyboard are translated to ASCII
Processor is then interrupted to indicate key press
Errors are detected and checked for

## Slide 13: Touchscreen Module
Allows single-touch touchscreen experience
Actual system uses spare Nintendo DS touchscreen
Simpler to implement than capacitive touchscreen
  May be switched to capacitive touchscreen in a later release

## Slide 14: SD Card Reader
Reads memory in 512 byte chunks
Used to load OS and programs
Saves to temporary memory, then transfers to permanent place
SD Card format required allows 16 programs and a 13 character title
  First block contains meta-data
  First program contains OS, which is automatically loaded by bootloader.

## Slide 15: Debugging Modules
Seven-segment display
  Easy to use, and guaranteed to work
  Displays 32-bit number, 16 bits at a time
Switches
  Allow flawless input for testing
  Simple interface makes it easy to capture
Libraries in C also support both of these with special, custom commands.

## Slide 16: Software Support
Assembler
  Assembles all assembly programs into binary
  Creates either coe or raw binary formats
  Includes pseudo-instruction la
MiniC Compiler
  Supports a large subset of ANSI C
  Includes other additions
McOS Operating System
  Simple, segmented OS
  One program may run at a time

## Slide 17: Challenges
Debugging
  Tricky due to not being able to simulate well
  Source of problems was not obvious
Regression Testing
  No easy way to test entire system at once
  Unit tests helped software, but no analog to hardware
Working with many different peripherals
  All of them had their own issues
  Not knowing exactly what the peripherals were doing.

## Slide 18: Current Status & Future
Currently ~80% finished
Working:
  32-bit processor
  Compiler/Assembler
  VGA Support
  SD Card Loading
In Progress:
  Phone Hardware
  Keyboard
  Resistive Touchscreen
  McOS

## Slide 19: Conclusions & Lessons Learned
Good learning tool for us and for others
Organization and architecture is key
  So is regression testing
Debugging techniques
  No break points, so print-outs instead
A task might be larger than it seems
Would recommend to any CSSE or ECE student

## Slide 20: Demo

## Slide 21: Questions???